Magnum Wax-Slabbing

Production System Specifications

Production Capacity

Production Time

Compressed Air

(One 8 inch Air Cylinder with 24 inch stroke)

(Standard Shop Air Compressor

is adequate for operation)

Water Flow

Water Temperature

Water Pressure

Water Volume

(Plates)

(Inlet & Outlet Manifold Pipes)

Electricity

Space

Actual

Working

(With Conveyor or packaging table between each system)

Lab Press

50 - 5 Kilo Slabs

1 - 2 hour pour to pour cycle time  4- 6 turns per 8 hr. shift

6 bar or greater

70 - 200 liters / minute

4 – 16 ºC

1.0 bar maximum.  Suggested pressure is .4-1.0 bar

24 Liters

290 Liters

None

.8 M X 3.5 M

3 M X 5 M

100 Plate System

200 - 5 Kilo Slabs or 1000 Kilo’s per cycle

1- 2 hour pour to pour cycle time  4- 6 turns per 8 hr. shift

6 bar or greater

290 - 770 liters / minute

4 – 16 ºC

1.0 bar maximum.  Suggested pressure is .4-1.0 bar

96 Liters

1140 Liters

None

.8M X 7.6 M

3 M X 9.0 M